## Slide 1: Analysis and Design of Arch Structures for the Oman Southern Expressway
Doug Jenkins - Interactive Design Services

## Slide 2: Introduction
Oman Southern Expressway
Embankment up to 34 metres high over arch culverts of 20 m and 15 m span.
Highest fill over a large span arch
Design challenges:
  Analysis and design of the arch profile to minimise bending moments and shear forces in the structure under very high soil loads.
  Design and detailing of skewed structures for asymmetric loads.
  Design of raft foundations for very high imposed loads.
  Analysis and design of double arch structures.

## Slide 3: Topics
The project
The design
  Analysis
  Provisions for high axial loads
  Skew structures
  Twin structures
  Raft foundations
  3D Analysis
Comparison with alternative arch shapes
recommendations for structures under high fills

## Slide 4: Project Description
55 km long highway project
Includes 7 large precast arch underpass structures, designed and supplied by Freyssinet International.
Arch sections: 15m x 7.5m and 20m x 10m
Maximum fill height increased from 24m to 34 m
Terraced retaining walls over the arches
Several skew structures
Double arches under the highest fills

## Slide 5: Typical 20m span double arch

## Slide 6: Analysis
2D, plane strain, FEA
Model the arch, foundations and backfill within the zone of influence of the arch.
Elasto-plastic soil model; soil stiffness and Poisson’s ratio related to confining pressure.
Soil loads are applied in stages reflecting the sequence of filling employed on site.
Add fill layer, then apply and remove a compaction load
Friction elements between the arch and the soil
The concrete is modelled as linear elastic

## Slide 7: Set up basic arch model

## Slide 8: Mesh Geometry

## Slide 9: Mesh Options, Material Properties, Loads, Parameters

## Slide 10: Generate mesh – run analysis

## Slide 11: Or for non standard projects – transfer mesh to general purpose FEA – Strand7

## Slide 12: Generated mesh; needs some work!

## Slide 13: Convert arch plate elements to beam elements on section CL + offset elements Subdivide long elements

## Slide 14: Convert arch/soil friction elements to friction contact elements + master/slave link

## Slide 15: Split elements at construction layers; insert links; assign elements of each layer to a separate group; separate fully fixed freedom case for each layer

## Slide 16: Apply compaction loads to each layer as a separate load case, and live loads to the top surface

## Slide 17: Adjust model as required

## Slide 18: Completed model

## Slide 19: Double Arch Model

## Slide 20: Set up analysis control parameters

## Slide 21: Construction Sequence

## Slide 22: Load Factors

## Slide 23: Plate Properties

## Slide 24: Run the analysis

## Slide 25: Run the analysis

## Slide 26: View results in Strand7

## Slide 27: Import and analyse results in Excel

## Slide 28: Plot Results and Member Capacities; Bending

## Slide 29: Reinforcement stresses

## Slide 30: Crack widths

## Slide 31: Shear Forces

## Slide 32: Moment/Axial Force Interaction Diagram

## Slide 33: Shear Force/Axial Force Interaction Diagram

## Slide 34: 3D Analysis

## Slide 35: 3D Analysis – using groups to create section views

## Slide 36: 3D Analysis – using groups to create section views

## Slide 37: Comparison with other arch shapes

## Slide 38: Comparison with other arch shapes

## Slide 39: Comparison with other arch shapes – flat ellipse

## Slide 40: RECOMMENDATIONS FOR ARCH STRUCTURES UNDER HIGH FILLS
High axial loads
  affected by the stiffness of the foundation soils and the type of foundation system.
  Include the foundation soils in the analysis
Non-optimised arch profiles may give rise to very high bending moments and shear forces.
  Flat elliptical profiles are particularly unsuited to high fills.
  Consider lower and upper bound stiffness parameters for both soil and structure
Significant savings to raft foundations by adjusting the depth of the slab between the footing sections .
Longitudinal effects may be significant
  Embankments with steep side slopes or high retaining walls,
  Structures on steep slopes.
  Structures on soft or variable foundation soils.

## Slide 41: More Information at:
http://www.interactiveds.com.au/software.html
http://newtonexcelbach.wordpress.com/